## Slide 1: CGM Common Hardware Platform

## Slide 2: What are we trying to do?
We need to get the data from the CGM Sensor so we can use it! The data can be stored any number of places but having it in the cloud allows access from anywhere by an approved user.
The sensors transmit over some kind of RF
  Dexcom G4 - 2.4 GHz ISM
  Medtronics 916.5 MHz ISM
  Dexcom G5 BLE
  Others ??
The challenge is to receive the sensor data and re-transmit the data to a location where it can be used for our own purposes.
We need the system to be small, unobtrusive, battery powered.
In order to upload the data no matter where you are we need multiple upload methods, BLE, WiFi, USB OTG, Direct Cellular

## Slide 3: Required Blocks
DexCom
RF Interface
(2.4 MHz ISM)
Medtronics
RF Interface
(924 MHz ISM)
Battery
Battery Fuel Gauge
Battery Charger
Controller/Uploader
BLE
WiFi
USB OTG
Cellular
Battery System
RF
Core Compute
Upload Interface

## Slide 4: Supported Configurations: Dexcom
Dexcom RF | Cellular Backhaul | Battery System |  | Parakeet
Dexcom RF | Core Processor | Wifi Backhaul | Battery System | 
Dexcom RF | Core Processor | BLE Backhaul | Battery System | 
Dexcom RF | BLE Backhaul | Battery System |  | DexDrip

## Slide 5: Supported Configurations: Medtronics
Medtronics RF | BLE Backhaul | Battery System |  | Riley Link?
Medtronics RF | Core Processor | Wifi | Battery System | 

## Slide 6: Hardware Optimizations
Can we make an RF module that will work for both 2.4GHz and 916.5 MHz?
  we will not likely be using both types of sensors so if we can use some external circuitry to select what frequency the RF needs to be and we can select the correct external antenna it would save space and power
Make the RF section a pluggable module
Make the Core processor a pluggable module
Make the backhaul modules plug directly into the RF modules
How does the battery system connect to the other modules?

## Slide 7: Software/Firmware Changes
The transmitter ID is not compiled into the FW
  make the transmitter ID configurable over the serial connection the RF module
  have a way from the application ( xdrip or others) to download the transmitter ID
Support different backhaul methods
  WiFi
  Cellular
  BLE
  USB OTG